## Slide 1
Alexander Brandl
ERHS 630
The System of Radiation Protection
Environmental and Radiological Health Sciences

## Slide 2
ICRP 26
  dose limits
    occupational exposure
    prevention of non-stochastic effects
    limitation of stochastic effects
ICRP 60
  exposure (practice and intervention)
    occupational, public, medical
  proposed and continuing practices
    justification, optimization, limitation
ICRP 103
  process- to situation-based
    planned, emergency, existing exposure situation
Progression and Evolution

## Slide 3
Individual dose limits
  50 mSv a-1 vs. 20 mSv a-1
    ICRP / IAEA and the U.S.
  “as low as possible”
  “as low as reasonably achievable, economic and social factors being taken into account” – (ALARA)
  “as low as reasonably practicable” – (ALARP) ?
ALARA
  has resulted in substantial decreases in individual doses
  reduced situations where dose limits play major role in system of protection
Consolidate and Develop

## Slide 4
Why ICRP 103?
  skepticism (international, stakeholder)
    “improving protection?”
    “new scientific basis?”
    “change to dose limits?”
Features
  updated wR and wT, radiation detriment
  maintaining 3 Fundamental Principles
  evolution from process- to situation-based approach
  maintaining individual dose limits in planned exposures
  re-enforcing the principle of optimization; dose and risk constraints (planned) and reference levels (emergency or existing)
  including approach for developing framework for protection of the environment
Consolidate & Develop (II)

## Slide 5
Scope of ICRP 103
  system of radiological protection applies
    to all exposures to ionizing radiation, regardless of size and origin
    however, source of exposure or pathways leading to dose must be amenable to control
    excluded, if deemed not amenable to control with regulatory instruments
    exempted, where controls are regarded as unwarranted
Consolidate & Develop (III)

## Slide 6
Characterization of possible exposure situations
Classification of types of exposure
Identification of exposed individuals
Categorization of types of assessment
  source-related
  individual-related
Precise formulation of the Principles of Protection
Level of individual doses which require protective actions
Conditions for the safety of radiation sources, including security, requirements for emergency preparedness and response
System of Protection

## Slide 7
Review of biological and epidemiological information on health risks
  distribution of relative risks for different organs or tissues; most notably for breast cancer and hereditary effects
  assuming LNT: combined detriment still  5 % Sv-1
  DDREF unchanged at 2
  prenatal exposure
    cancer risk similar to irradiation in early childhood
    threshold for induction of malformations and severe mental retardation
  retention of dose limits for effective and equivalent dose
    further information and revision might be needed (i.e., eye)
  data on possible non-cancer diseases insufficient
Scientific Basis

## Slide 8
No fundamental changes to the system of radiation protection needed (ICRP 60)
Numerical recommendations (ICRP 60) mostly remain valid
ICRP 103 should not imply major changes to radiation protection regulations (if based on ICRP 60 and subsequent policy guidance documents)
LNT still basis for summation of doses from external exposure and intake of radionuclides
Doses are calculated using reference computational phantoms; effective dose calculated to Reference Person not an individual
ICRP Conclusions

## Slide 9
Effective dose
  intended for use as protection quantity
  prospective dose assessment for planning and optimization, demonstration of compliance with regulatory dose limits
  not recommended for epidemiological evaluations, detailed specific retrospective investigations of individual exposure and risk
Collective effective dose
  instrument for optimization, comparing radiological technologies and protection procedures
  mainly in occupational settings
  not intended as a tool for epidemiological risk assessment
  inappropriate in risk projections (calculation of cancer deaths from trivial individual doses to be avoided)
Effective Dose

## Slide 10
Planned exposure situations
  planned introduction and operation of sources
  includes situations previously termed “practices”
Emergency exposure situations
  unexpected situations requiring urgent attention
    occurring during operation of a planned situation
    malicious act
Existing exposure situations
  already exist when a decision on control has to be taken
    natural background radiation
Exposure Situations

## Slide 11
Justification
  any decision that alters the radiation exposure situation should do more good than harm
Optimization of Protection
  the likelihood of incurring exposure, the number of people exposed, and the magnitude of their individual doses should all be kept as low as reasonably achievable, taking into account economic and societal factors
Application of Dose Limits (planned exposures only!)
  the total dose to any individual from regulated sources in planned exposure situations other than medical exposure should not exceed the appropriate limits
Fundamental Principles

## Slide 12
Categories of exposure
  occupational
  public
    upon declaration of pregnancy: embryo / fetus
  medical
    patients
    comforters, carers, volunteers in research
Fundamental Principles (II)

## Slide 13
Any decision-making process should explicitly include expected changes in radiation detriment
Consequences considered not confined to radiation protection
  need to include other risks, cost-benefit of the activity
Requirement that net benefit be positive!
  planned exposures: only to be introduced if net benefit to the individual or society as a whole offsets radiation detriment
  emergency or existing exposures: decisions taken to reduce doses should do more good than harm
Justification

## Slide 14
Some exposure scenarios deemed unjustified by ICRP
  deliberate addition or activation of radionuclides in food, beverages, cosmetics, toys, personal jewelry and adornments
  radiological examination for occupational, health insurance, or legal purposes undertaken without reference to clinical indications (exceptions: expected important information on the health of the individual, important criminal investigation)
  medical screening of asymptotic population groups, unless advantages for the individual or society as a whole outweigh costs and detriment
Justification (II)

## Slide 15
Only for justified exposure situations
Source-related process
Aimed at achieving best level of protection under the prevailing circumstances
Iterative process, involving:
  evaluation of the exposure situation, including any potential exposures
  selection of an appropriate value for constraints or reference levels
  identification of potential protection options
  selection of the best option (cost-benefit) under the prevailing circumstances
  implementation of selected option
Optimization

## Slide 16
Limitation
ICRP dose limits
  “not” changed from ICRP 60
  (from ICRP 103)

## Slide 17
Key role of optimization emphasized
Restrictions are applied to doses to a nominal individual (Reference Person)
  dose constraints
    planned exposure situations
  reference levels
    emergency and existing exposure situations
Options where E  constraint, should be rejected at planning stage
  applied prospectively (optimization!)
After optimization is completed and E  constraint
  reasons to be investigated
  regulatory action not necessarily prompted
Dose Constraints

## Slide 18
Limits and Constraints
Dose limits vs. dose constraints or reference levels
  workers and members of the public
  (from ICRP 103)

## Slide 19
Limits and Constraints (II)
Dose limits, dose constraints, and reference levels
  (from ICRP 103)

## Slide 20
Limits and Constraints (III)
Dose constraints and reference levels
  (from ICRP 103)

## Slide 21
Previously managed as practices
  includes: protection during medical uses of ionizing radiation
    patients, comforters, carers, volunteers in biomedical research
Planning of planned exposure situations
  to include deviations from normal operating procedures
  potential exposures
    accidents or malicious events
    not planned, but can be anticipated
Designer and user of sources
  reduction of likelihood for potential exposures
  assessment of likelihood and installation of engineering safeguards
Planned Exposures

## Slide 22
Reference levels
  residual dose after implementation of measures should be below reference levels
    total dose regulator plans not to exceed in an emergency
  for optimization use of averted dose
Emergency preparedness
  planning for the implementation of optimized protection strategies
    purpose: reducing exposures to below the reference level
Emergency response
  reference level acts as benchmark for evaluating effectiveness of protective actions
  input in establishing need for further actions
Emergency Exposures

## Slide 23
Exposure situations
  naturally occurring exposures
  past events
  past accidents
Protection strategies
  often implemented in an interactive, progressive manner
  over many years
Existing Exposures

## Slide 24
Example
  222Rn in dwellings and workplaces
  recent epidemiological studies
    confirm health risk from radon
    provide support for recommendations on protection against radon
  national reference levels
    for the sake of continuity and practicability
    E < 10 mSv a-1 (600 Bq m-3) in dwellings
  in workplaces: E  reference level
    occupational exposure
  optimization even if E < reference level
Existing Exposures (II)

## Slide 25
Radiation protection of the environment
  previously
    concern mainly for transfer of radionuclides through the environment
    context of planned exposure situations
  protection of the general public
    would ensure that other species are not put at risk
  scientifically sound framework for protection of the environment in all exposure situations
    use of Reference Animals and Plants
    doses calculated for reference organisms could be compared to doses known to have specific biological effects (at a given dose rate)
  no dose limits
Environment