## Slide 1
Alexander Brandl
ERHS 630
Exposure and Dose
Environmental and Radiological Health Sciences

## Slide 2
Quantitatively relates
  measurements made in a radiation field
  to chemical / biological changes the radiation would produce in a target
Quantifies
  the incidence of various biological changes
  as a function of radiation received
  dose-effect relationship
Radiation Dosimetry

## Slide 3
Interaction between radiation and target atoms or molecules results in
  excitation
  ionization
  secondary electrons
Secondary electrons
  can be “ionizing”
  produce additional excitation and ionization
Radiation / Target

## Slide 4
Interaction occurs “locally” within the path of a charged particle
Chemical / biological effects
  electronic transitions producing chemically active species completed in very short time (≤ 10-15 s)
  due to direct absorption of energy from the radiation by the target
Interaction forms basis for
  radiation dosimetry
  radiation instrumentation
Radiation / Target (II)

## Slide 5
Energy Transfer
Ionization / excitation
Secondary particles
Delta rays
Threshold energy for ionization
(from ICRU 16)

## Slide 6
Energy Transfer (II)
Energy deposited within volume element (mass) of interest (from ICRU 16)?

## Slide 7
Definition of “local?”
How to account for energy leaving the volume element (mass)?
Dependence on
  energy of incident radiation
  radiation type (“quality”)
Need to find radiation quantities, which allow quantification of
  physical observables
  biological effects
Energy Transfer (III)

## Slide 8
Generally
  non-uniform in space
  variable in time
Quantities
  often depend on discrete interactions between radiation and atoms
  would require:
    volume (mass) small enough that further reduction in size does not change the measured quantity
    large enough to contain many interactions and be traversed by many particles
Definitions of these quantities must include appropriate averaging procedures
Radiation Fields

## Slide 9
Physical quantity
Defined only for X-rays and gamma radiation
Energy transfer to air
  ionization (charge) produced in air
  charge per unit mass
  air at STP (standard temperature and pressure)
Exposure

## Slide 10
Sum of the electrical charge of all ions of one sign produced in air
Divided by the mass of air in a certain volume element
Provided: all electrons produced in the volume element (“suitably small”) are completely stopped in air
SI unit [C kg-1]
Old unit [R], the Roentgen
Exposure (II)

## Slide 11
The Roentgen:
  charge of 1 esu in 1 cm3 of air
Exposure (III)

## Slide 12
Physical quantity
Defined for all types of ionizing radiation
Energy transfer to any target
  energy absorbed per unit mass in the material
  treated as a point function, having a value at any position in an irradiated object
Absorbed Dose

## Slide 13
Energy Imparted:
  radiant energy incident on matter (Rin), sum of all charged and uncharged particles entering a volume element
  minus radiant energy emerging from that volume element, (Rout)
  changes of rest mass energy are included in SQ
Expectation value of : mean energy imparted ()
Absorbed Dose (II)

## Slide 14
Mean energy imparted by ionizing radiation to matter
Divided by the mass of the irradiated material (volume)
SI unit [J kg-1] or “Gray” [Gy]
Old unit [rad], the “radiation absorbed dose”
Absorbed Dose (III)

## Slide 15
The rad:
  absorbed energy of 100 ergs in 1 g
Absorbed Dose (IV)

## Slide 16
Relating exposure to absorbed dose:
  electromagnetic radiation only
  in air
Absorbed Dose (V)

## Slide 17
How about the Roentgen?
  in air
Absorbed Dose (VI)

## Slide 18
Physical quantity
Defined for indirectly ionizing radiation (photons, neutrons)
Energy transfer to any target
  kinetic energy of all charged particles produced by the radiation per unit mass
  dimensions of absorbed dose
SI unit [J kg-1] or “Gray” [Gy]
Kerma

## Slide 19
Comparison: kerma versus absorbed dose
  absorbed dose builds up behind a surface to a depth comparable with the range of the secondary charged particles
  kerma decreases in material, as the incident particles are being attenuated
  identical if all kinetic energy is absorbed “locally”
    charged particle equilibrium
    bremsstrahlung losses negligible
Kerma (II)

## Slide 20
Physical quantity
Defined for charged particles
Mean energy transfer per unit distance along a charged particle track
  initially synonymous with stopping power
  now: “restricted” versus “unrestricted” stopping power
SI unit [J m-1], more commonly [keV mm-1]
Linear Energy Transfer

## Slide 21
Quantities with which, by means of their measurements, compliance with the system of protection may be demonstrated
  Ambient dose equivalent
H*(d)
  Directional dose equivalent
H’(d,W)
  Personal dose equivalent
Hp(d)
Operational Quantities

## Slide 22
Dosimetric quantities specified in the human body by ICRP
  organ absorbed dose
DT
  organ equivalent dose
HT
  effective dose
E
Protection Quantities

## Slide 23
Equivalent dose
  in organ or tissue T
  due to radiation R
SI unit [J kg-1] or “Sievert” [Sv]
Old unit [rem], the “Roentgen equivalent man”
Equivalent Dose

## Slide 24
Effective dose
  in the whole body
  due to radiation R
SI unit [J kg-1] or “Sievert” [Sv]
Old unit [rem], the “Roentgen equivalent man”
Effective Dose

## Slide 25
System of Quantities
Dosimetric quantities for external radiation (from ICRP 74 / ICRU 57)